## Slide 1: Coffee Roaster Project
Arduino & Android

## Slide 2: Overview
Arduino
  ESP32
Android
  Android studio

## Slide 3: Goal
MAX 6675
  Collecting temperature dynamically
ESP32s
  Translate analogy signal change to digital
  Via Bluetooth transmit data to phone
Android
  Receive data from ESP32s
  Show the curve visually
  Start, Record temperature, End
  Save file in local (.csv .jpg)

## Slide 4: Layout
ESP32s
MAX 6675
phone
screen

## Slide 5: Flow
ESP32s
MAX 6675
MSG: 23 °C
Bluetooth Adapter
Input Stream
Bluetooth Socket
Find Bluetooh Device
bluetoothSocket.getInputStream()
updateLineChart()
Geisha
start
stop
record
mainActivity
Geisha
browseHistoryDataActivity
Description
blutoothOutOffRangeActivity
Please get back to device !
Save file()
FileName
Save file
saveFileActivity
Description
Folder

## Slide 6: mainActivity
Update linechart
Start
  Draw
  Start to count
Record
  Draw temperature point
Stop
  Stop to Draw
  Stop to count
  Jump to saveFileActivity
Geisha
start
stop
record

## Slide 7: saveFileActivity
filename
  Type in
Folder
  Show default folder in textbox
  Can type directory directly or browse
Description
  More blank option ? Ex. Region, Height, …
FileName
Save file
Description
Folder

## Slide 8: bluetoothOutOffRangeActivity
Show warning view & counting down (cntDownPeriod = 15 sec ?)
Make warning sound
ESP32
  Stored lost data in ESP32 (need SD card ?)
  Decided how many storage need for exception data storage
    If out off time, you will lose data
  If recover, back to mainActivity and restored lost data
Please get back to device !

## Slide 9: browseHistoryDataActivity
Show title & lineChart & description
Press back-button back to mainActivity
Geisha
Description

## Slide 10: interface
Arduino & Android
  Bluetooth interface

## Slide 11: testcases
User out off Bluetooth range
  Android: give caution closer to devices in case of losing data
  Arduino: extra space to store the data when user out of range (SD card)
    Need to deal with specific circumstance (還沒想到怎摩處理)